Bill of Materials

Open-source USB-A magnetic breakaway connector used in the BusKill laptop kill cord
This BOM is in progress

Component		Base QTY	Link (if applicable)
USB male		1
USB female (10 mm)		1
Hexagonal neodymium magnets		4	See vendor list
Pogo pins Working height: 0.298" (7.58mm)		8	See vendor list
M1 Screws		4
M1 Nut		4
3D printed shell			Part Design in development
	Input side top	1
	Input side bottom	1
	Output side top	1
	Output side bottom	1