BusKill Defcon32 Demo Lab Outline
1. Introduction (2 mins)
  1. Who is BusKill?
  2. Project Goal
  3. Project Rationale
2. Get to know the audience (2 mins)
  1. Raise hand if
    1. Have ever heard of BusKill
    2. Have a 3D printer
    3. Use Kali? Use QubesOS? Use Tails?
3. Software Capabilities (5 mins)
  1. Lock screen / Shutdown (less than 1 min)
  2. Luks Header Shredder (1 min) forensically proven with bulk extractor
  3. Qubes
  4. Limitations
4. Hardware Requirements (3 mins)
  1. Establishes physical security from computer to person
  2. Disconnects usb easily, but not too easily
  3. Able to dissemble for inspection
  4. Doesn’t block neighboring ports
5. Supplier Version (1 min)
  1. Components list
  2. Where to find in Repo
6. 3D-Printed Version (2 mins)
  1. Components list
  2. Where to find in Repo
  3. Demo
7. Hardware Development History and Philosophy (10 mins)
        1. Parametric design in OpenSCAD
        2. Milestones
            1. Choosing parts (considerations for pogo pins, receptors, usbs)
            2. Trying to splice it, frying the USB drives
            3. The magnets (hexagonal, Nstrength, disc/cube)
        3. Constraints
        4. OpenSCAD code tour
8. How to help and FAQ (6 mins)
  1. Build it
  2. Make the case smaller
  3. Make assembly easier
  4. Identify cheaper and more easily sourced components
  5. Make the code more parametric